## Slide 1: AccelWattch: A Power Modeling Framework for Modern GPUs
Vijay Kandiah, Scott Peverelle, Mahmoud Khairy, Junrui Pan, Amogh Manjunath, Timothy G. Rogers, Tor M. Aamodt, Nikos Hardavellas
MICRO’21 54th Annual IEEE/ACM International Symposium on Microarchitecture
October 18-21, 2021
Virtual Event, Greece
Notes: Hello everyone, I am Vijay Kandiah from Northwestern University and I’m going to talk to you about AccelWattch.

## Slide 2
Widespread adoption of GPUs (AI, machine learning, HPC, ...)
  70% of top 50 HPC applications are GPU-accelerated
  29% of TOP500 supercomputer systems are GPU-accelerated (and growing)
MICRO-54
GPUs Are Important Systems
Notes: GPUs have become important architectures in various domains like Artificial Intelligence, Machine Learning, and High-Performance Computing.
29% of systems in the most recent TOP500 supercomputer list are now GPU-accelerated.
A vast majority of these GPU-Accelerated systems employ an NVIDIA Volta GPU chip.
As GPUs market share grows, so has their overall power consumption.

## Slide 3: Performance per Watt Is the New Moore’s Law
MICRO-54
Notes: At the same time, performance per watt has become a very important metric.
It has been argued that the future will be measured in performance per watt.

## Slide 4: The Need for a New GPU Power Model
Computer architects need tools to estimate performance AND power
MICRO-54
Notes: Thus, GPU architects require robust tools that will enable them to quickly and accurately model both the performance and the power comsumption of modern GPUs

## Slide 5: The Need for a New GPU Power Model
Computer architects need tools to estimate performance AND power
GPU performance modeling has progressed in great strides
   but GPU power modeling has lagged
MICRO-54
Notes: However, while GPU performance modeling has progressed in great strides, GPU power modeling has lagged behind.

## Slide 6: The Need for a New GPU Power Model
Computer architects need tools to estimate performance AND power
GPU performance modeling has progressed in great strides
   but GPU power modeling has lagged
Current state-of-the-art, GPUWattch, inaccurate for modern architectures
MICRO-54
We Need a New Cycle-level Power Model for Modern GPUs!
Notes: GPUWattch has been a popular tool to model, at cycle-level, the power consumption of new innovations in GPU architectures,
but it was designed to model and was validated against older architectures which have fewer energy efficiency optimizations.
As a result, Attempting to model recent GPUs such as Volta using GPUWattch produces significant inaccuracies. For instance, we have seen average errors of 225% when modeling Volta with GPUWattch.
Thus, a new accurate power model is needed for modern GPUs, and we tackle this problem in this work by introducing AccelWattch.

## Slide 7: AccelWattch: A Power Model for Modern GPUs
Models Constant, Static, Dynamic power accounting for
  DVFS
  Power gating
  Thread divergence
  Intra-warp functional unit overlap
  Variable SM occupancy
Allows trade offs in accuracy vs. modeling flexibility and effort; driven by
  Emulation (PTX) & trace-driven (SASS) performance models
  Hardware performance counters
  or a combination of above
Highly accurate for modern GPUs
  7.5 – 9.2% mean abs. error for Volta GV100
  22 – 24× lower error than GPUWattch
  Accurate for design space exploration (1 – 3% avg. error in relative power estimates)
MICRO-54
Notes: AccelWattch is a configurable cycle-level GPU power model for the NVIDIA Volta GPU architecture.
AccelWattch accurately captures constant, static, and dynamic power consumption in the presence of DVFS, power gating, thread divergence, Intra-warp functional unit overlap and variable SM occupancy.
AccelWattch can be driven by emulation and trace-driven software performance models, or by hardware performance counters obtained from execution on real silicon or by a combination of the two. Thus, AccelWattch allows trade offs in accuracy vs. modeling flexibility and modeling effort. To the best of our knowledge, AccelWattch is the first model to allow such trade offs.
We show that AccelWattch is highly accurate for the Volta GV100 GPU.
Finally, we show that AccelWattch enables reliable design space exploration.

## Slide 8: DVFS-Aware Constant Power Model
Chart: Processor Frequency (GHz)
| 0.13500000000000001 | 0.20200000000000001 | 0.35199999999999998 | 0.502 | 0.65200000000000002 | 0.80200000000000005 | 1.0049999999999999 | 1.1020000000000001 | 1.2 | 1.35 | 1.4470000000000001
NANOSLEEP | 32.715 | 32.77 | 33.3833 | 35.0367 | 36.03 | 37.1967 | 41.32 | 43.7267 | 46.37 | 52.5475 | 56.94
Modeled | 27.2449 | 29.5338 | 30.6698 | 33.2131 | 35.7565 | 38.2998 | 40.8431 | 44.285 | 45.9297 | 47.5913 | 50.1346 | 51.7792
MICRO-54
Dynamic Power
Static Power
Notes: Total power can be modeled as the sum of three terms representing dynamic, static and constant power.
The dynamic power term is capacitance * voltage-squared * frequency
The static power term is some constant * voltage
Finally, the constant power term corresponds to the power consumed by components such as GPU board fans and peripheral circuitry.
In the prior model, GPUWattch, all terms except frequency are assumed to be constant. Thus, total power is linear in frequency.
As frequency approaches zero, the dynamic power is zeroed out and static and constant power are lumped together in a new term that can be calculated by looking at the y-intercept

## Slide 9: DVFS-Aware Constant Power Model
Chart: Processor Frequency (GHz)
| 0.13500000000000001 | 0.20200000000000001 | 0.35199999999999998 | 0.502 | 0.65200000000000002 | 0.80200000000000005 | 1.0049999999999999 | 1.1020000000000001 | 1.2 | 1.35 | 1.4470000000000001
MIX | 38.7333 | 38.7933 | 45.3025 | 68.5 | 81.9467 | 91.6769 | 121.922 | 140.24 | 162.15 | 203.69 | 239.43
INT_ADD | 35.1367 | 35.28 | 37.96 | 47.87 | 53.492 | 60.5875 | 73.3125 | 81.589 | 99.2683 | 111.6017 | 129.9225
FP_ADD | 35.01 | 35.035 | 37.77 | 48.0675 | 51.558 | 56.1533 | 69.68 | 77.0206 | 88.104 | 106.584 | 121.612
FP_MUL | 34.6833 | 34.9767 | 37.8 | 47.0425 | 53.148 | 58.8733 | 70.0433 | 77.8115 | 86.8636 | 105.327 | 122.418
NANOSLEEP | 32.715 | 32.77 | 33.3833 | 35.0367 | 36.03 | 37.1967 | 41.32 | 43.7267 | 46.37 | 52.5475 | 56.94
Modeled | 27.2449 | 29.5338 | 30.6698 | 33.2131 | 35.7565 | 38.2998 | 40.8431 | 44.285 | 45.9297 | 47.5913 | 50.1346 | 51.7792
MIX model | -1.4502 | 17.8121 | 27.3718 | 48.7744 | 70.1769 | 91.5794 | 112.9819 | 141.9466 | 155.7869 | 169.7699 | 191.1724 | 205.0127
INT_ADD model | 15.4357 | 24.6357 | 29.2016 | 39.4238 | 49.646 | 59.8682 | 70.0905 | 83.9245 | 90.5349 | 97.2134 | 107.4356 | 114.046
FP_ADD model | 17.2311 | 25.518 | 29.6307 | 38.8384 | 48.0461 | 57.2537 | 66.4614 | 78.9225 | 84.8767 | 90.8924 | 100.1001 | 106.0544
FP_MUL model | 17.4589 | 25.744 | 29.8559 | 39.0616 | 48.2674 | 57.4731 | 66.6789 | 79.1373 | 85.0903 | 91.1047 | 100.3105 | 106.2635
MICRO-54
Dynamic Power
Static Power
-2W?
27W?
15W?
Notes: The GPUWattch methodology, though, is unreliable when applied to modern GPUs that have DVFS and Voltage is dependent on frequency.
After following the methodology on a variety of sample executing kernels, it is unclear what the static+constant power is.
is it 27W? or 15W? Or, God forbid, negative 2W?
[[[ note for you: if you model it as a quadratic polynomial, then the static power becomes negative, as much as -34W. ]]]

## Slide 10: DVFS-Aware Constant Power Model
Chart: Processor Frequency (GHz)
| 0.13500000000000001 | 0.20200000000000001 | 0.35199999999999998 | 0.502 | 0.65200000000000002 | 0.80200000000000005 | 1.0049999999999999 | 1.1020000000000001 | 1.2 | 1.35 | 1.4470000000000001
MIX | 38.7333 | 38.7933 | 45.3025 | 68.5 | 81.9467 | 91.6769 | 121.922 | 140.24 | 162.15 | 203.69 | 239.43
INT_ADD | 35.1367 | 35.28 | 37.96 | 47.87 | 53.492 | 60.5875 | 73.3125 | 81.589 | 99.2683 | 111.6017 | 129.9225
FP_ADD | 35.01 | 35.035 | 37.77 | 48.0675 | 51.558 | 56.1533 | 69.68 | 77.0206 | 88.104 | 106.584 | 121.612
FP_MUL | 34.6833 | 34.9767 | 37.8 | 47.0425 | 53.148 | 58.8733 | 70.0433 | 77.8115 | 86.8636 | 105.327 | 122.418
NANOSLEEP | 32.715 | 32.77 | 33.3833 | 35.0367 | 36.03 | 37.1967 | 41.32 | 43.7267 | 46.37 | 52.5475 | 56.94
Modeled | 32.7043 | 32.8978 | 33.0272 | 33.4802 | 34.2798 | 35.5737 | 37.5096 | 41.4146 | 43.8979 | 46.8677 | 52.4042 | 56.6829
MIX model | 31.9469 | 38.3907 | 41.7922 | 50.4081 | 61.1441 | 74.9036 | 92.5902 | 124.3876 | 143.3582 | 165.3438 | 205.0565 | 235.0099
INT_ADD model | 31.5495 | 34.5647 | 36.1593 | 40.2121 | 45.2878 | 51.8223 | 60.2516 | 75.4524 | 84.5381 | 95.0779 | 114.1346 | 128.5194
FP_ADD model | 32.9583 | 35.2088 | 36.4215 | 39.6078 | 43.7924 | 49.4009 | 56.8586 | 70.6536 | 79.0238 | 88.8081 | 106.6384 | 120.1806
FP_MUL model | 32.2436 | 34.8541 | 36.2397 | 39.7849 | 44.2686 | 50.0908 | 57.6516 | 71.364 | 79.5882 | 89.1454 | 106.4569 | 119.5432
Chart: Processor Frequency (GHz)
| 0.13500000000000001 | 0.20200000000000001 | 0.35199999999999998 | 0.502 | 0.65200000000000002 | 0.80200000000000005 | 1.0049999999999999 | 1.1020000000000001 | 1.2 | 1.35 | 1.4470000000000001
MIX | 38.7333 | 38.7933 | 45.3025 | 68.5 | 81.9467 | 91.6769 | 121.922 | 140.24 | 162.15 | 203.69 | 239.43
INT_ADD | 35.1367 | 35.28 | 37.96 | 47.87 | 53.492 | 60.5875 | 73.3125 | 81.589 | 99.2683 | 111.6017 | 129.9225
FP_ADD | 35.01 | 35.035 | 37.77 | 48.0675 | 51.558 | 56.1533 | 69.68 | 77.0206 | 88.104 | 106.584 | 121.612
FP_MUL | 34.6833 | 34.9767 | 37.8 | 47.0425 | 53.148 | 58.8733 | 70.0433 | 77.8115 | 86.8636 | 105.327 | 122.418
NANOSLEEP | 32.715 | 32.77 | 33.3833 | 35.0367 | 36.03 | 37.1967 | 41.32 | 43.7267 | 46.37 | 52.5475 | 56.94
Modeled | 27.2449 | 29.5338 | 30.6698 | 33.2131 | 35.7565 | 38.2998 | 40.8431 | 44.285 | 45.9297 | 47.5913 | 50.1346 | 51.7792
MIX model | -1.4502 | 17.8121 | 27.3718 | 48.7744 | 70.1769 | 91.5794 | 112.9819 | 141.9466 | 155.7869 | 169.7699 | 191.1724 | 205.0127
INT_ADD model | 15.4357 | 24.6357 | 29.2016 | 39.4238 | 49.646 | 59.8682 | 70.0905 | 83.9245 | 90.5349 | 97.2134 | 107.4356 | 114.046
FP_ADD model | 17.2311 | 25.518 | 29.6307 | 38.8384 | 48.0461 | 57.2537 | 66.4614 | 78.9225 | 84.8767 | 90.8924 | 100.1001 | 106.0544
FP_MUL model | 17.4589 | 25.744 | 29.8559 | 39.0616 | 48.2674 | 57.4731 | 66.6789 | 79.1373 | 85.0903 | 91.1047 | 100.3105 | 106.2635
MICRO-54
Dynamic Power
Static Power
Dynamic Power
Static Power
-2W?
27W?
15W?
32.5W
Notes: Recently-published data for fully-realized processors show a near-linear relationship in the frequency-voltage curve.
When we approximate the voltage in modern GPUs as a linear function of frequency, we can rewrite the total power equation as a cubic polynomial on frequency with a missing quadratic term.
These polynomials show strong correlation to hardware power measurements. When the GPU frequency is 0, curves for all sample executing kernels converge at around 32.5W.
This is our AccelWattch modeled constant power for Volta.

## Slide 11: Power-Gating-Aware Static Power Model
Aggressive power gating at different levels
MICRO-54
Notes: After estimating constant power, we move on to modeling static power in the presence of power gating.
Modern GPUs employ power-gating for chip-wide, SM-wide, and lane-specific hardware components.

## Slide 12: Power-Gating-Aware Static Power Model
Chart: Measured Power (W)
| Inactive Chip
Constant | 32.5071 | 0 | 0 | 0 | 0 | 0 | 0
Chip Global | 0 | 0 | 0 | 0 | 0 | 0 | 0
SM Activation | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addl. Lanes | 0 | 0 | 0 | 0 | 0 | 0 | 0
MICRO-54
Chip is inactive  only Const. power
Notes: When no SMs are active on the chip, it consumes only the constant power which we estimated previously to be 32.5W.

## Slide 13: Power-Gating-Aware Static Power Model
Chart: Measured Power (W)
| Inactive Chip | 1 Lane × 1 SM
Constant | 32.5071 | 32.5071
Chip Global | 0 | 23.2472
SM Activation | 0 | 0.49821
Addl. Lanes | 0 | 0
MICRO-54
Power up first SM  Powers up global components (L2, NoC, MC, etc.)
first SM lane on chip
(activating first SM)
Notes: When a kernel uses only one lane on one SM, the activation of that first SM powers up global chip structures such as L2 Cache and Memory Controllers and activates SM-wide structures for that SM such as the L1 cache.

## Slide 14: Power-Gating-Aware Static Power Model
Chart: Measured Power (W)
| Inactive Chip | 1 Lane × 1 SM | 1 Lane × 80 SMs
Constant | 32.5071 | 32.5071 | 32.5071
Chip Global | 0 | 23.2472 | 23.2472
SM Activation | 0 | 0.49821 | 39.8571
Addl. Lanes | 0 | 0 | 0
MICRO-54
Power up all 80 SMs  only 1.7× increase in power for 79× more SMs
first SM lane on chip
(activating first SM)
+79 lanes, 1 per SM
(activating +79 SMs)
Notes: When the same kernel uses one lane on all SMs, each additional SM powers up only its SM-wide structures. The global chip structures have already been powered up. As a result, we notice only a 1.7x increase in power even though we have 79x more SMs.

## Slide 15: Power-Gating-Aware Static Power Model
Chart: Measured Power (W)
| Inactive Chip | 1 Lane × 1 SM | 1 Lane × 80 SMs | 8 Lanes × 80 SMs | 16 Lanes × 80 SMs | 24 Lanes × 80 SMs | 32 Lanes × 80 SMs
Constant | 32.5071 | 32.5071 | 32.5071 | 32.5071 | 32.5071 | 32.5071 | 32.5071
Chip Global | 0 | 23.2472 | 23.2472 | 23.2472 | 23.2472 | 23.2472 | 23.2472
SM Activation | 0 | 0.49821 | 39.8571 | 39.8571 | 39.8571 | 39.8571 | 39.8571
Addl. Lanes | 0 | 0 | 0 | 9.1356 | 24.6846 | 48.0986 | 60.9319
MICRO-54
Power up all lanes  only 1.6× increase in power for 31× more lanes
+2480 lanes
+1840 lanes
+1200 lanes
+560 lanes
first SM lane on chip
(activating first SM)
+79 lanes, 1 per SM
(activating +79 SMs)
Notes: In a similar fashion, when the same kernel uses additional threads in each SM, it powers up only the functional units of these additional lanes. As a result, when all lanes are active, we notice only a 1.6x increase in power even though we have 31x more lanes.

## Slide 16: Power-Gating-Aware Static Power Model
Chart: Measured Power (W)
| Inactive Chip | 1 Lane × 1 SM | 1 Lane × 80 SMs | 8 Lanes × 80 SMs | 16 Lanes × 80 SMs | 24 Lanes × 80 SMs | 32 Lanes × 80 SMs
Constant | 32.5071 | 32.5071 | 32.5071 | 32.5071 | 32.5071 | 32.5071 | 32.5071
Chip Global | 0 | 23.2472 | 23.2472 | 23.2472 | 23.2472 | 23.2472 | 23.2472
SM Activation | 0 | 0.49821 | 39.8571 | 39.8571 | 39.8571 | 39.8571 | 39.8571
Addl. Lanes | 0 | 0 | 0 | 9.1356 | 24.6846 | 48.0986 | 60.9319
MICRO-54
 The power model should treat the first lane differently than the rest!
+2480 lanes
+1840 lanes
+1200 lanes
+560 lanes
first SM lane on chip
(activating first SM)
+79 lanes, 1 per SM
(activating +79 SMs)
AccelWattch captures these effects!
Notes: So what does all that mean?
The power model should treat the first lane differently than the rest!
AccelWattch captures these effects as we will see next.

## Slide 17: Divergence-Aware Static Power Model
MICRO-54
Linear Model
Notes: The natural way to account for power consumption difference between the first and additional lanes is to model static power by this equation where y is the number of active lanes.
The Pstatic,firstlane term includes the static power of SM-wide components.
Each additional active lane contributes its own functional unit’s static power which is represented by Pstatic,addlane.
We refer to this equation as the linear static power model

## Slide 18: Divergence-Aware Static Power Model
Chart: INT_MUL
| 1 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32
Measured | 100.6108 | 101.8406 | 110.1956 | 118.91 | 127.56 | 113.74 | 117.355 | 120.468 | 123.76
Linear Model | 99.5314 | 101.7065 | 104.6067 | 107.5068 | 110.407 | 113.3071 | 116.2073 | 119.1074 | 122.0076
MICRO-54
Linear Model
Notes: However, the linear static power model does not always match real-world observations.
When we measure the power of a microbenchmark on real silicon that issues integer multiply operations with varying threads per warp, we observe significant deviation from the linear model.
(next slide)
Volta has 4 processing blocks per SM and only 16 integer functional units per processing block.
Thus, a warp executes in half-warp steps.
(next slide)
If there are only 16 active threads in a warp, then the first 16 active-thread half-warp always executes, ...
(next slide)
...but the system forgoes the execution of the 2nd empty half-warp.
(next slide)
Thus, one full half-warp...
(next slide)
...executes after another.
(next slide)
Hence, the system runs at full int multiply utilization and reaches maximum power.
Similarly, when there are 32 active threads per warp, then both half-warps fully utilize functional units, and the system again reaches power close to the maximum.
(next slide)
If, however, we have 20 active threads, then the execution of full half-warps...
(next slide)
...is interleaved with mostly empty ones that have only 4 active threads.
(next slide)
...and this behavior...
(next slide)
...repeats.
(next slide)
Thus, the overall power consumption drops even though the energy consumption per warp instruction is higher.

## Slide 19: Divergence-Aware Static Power Model
Chart: INT_MUL
| 1 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32
Measured | 100.6108 | 101.8406 | 110.1956 | 118.91 | 127.56 | 113.74 | 117.355 | 120.468 | 123.76
Linear Model | 99.5314 | 101.7065 | 104.6067 | 107.5068 | 110.407 | 113.3071 | 116.2073 | 119.1074 | 122.0076
MICRO-54
Notes: However, the linear static power model does not always match real-world observations.
When we measure the power of a microbenchmark on real silicon that issues integer multiply operations with varying threads per warp, we observe significant deviation from the linear model.
(next slide)
Volta has 4 processing blocks per SM and only 16 integer functional units per processing block.
Thus, a warp executes in half-warp steps.
(next slide)
If there are only 16 active threads in a warp, then the first 16 active-thread half-warp always executes, ...
(next slide)
...but the system forgoes the execution of the 2nd empty half-warp.
(next slide)
Thus, one full half-warp...
(next slide)
...executes after another.
(next slide)
Hence, the system runs at full int multiply utilization and reaches maximum power.
Similarly, when there are 32 active threads per warp, then both half-warps fully utilize functional units, and the system again reaches power close to the maximum.
(next slide)
If, however, we have 20 active threads, then the execution of full half-warps...
(next slide)
...is interleaved with mostly empty ones that have only 4 active threads.
(next slide)
...and this behavior...
(next slide)
...repeats.
(next slide)
Thus, the overall power consumption drops even though the energy consumption per warp instruction is higher.

## Slide 20: Divergence-Aware Static Power Model
Chart: INT_MUL
| 1 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32
Measured | 100.6108 | 101.8406 | 110.1956 | 118.91 | 127.56 | 113.74 | 117.355 | 120.468 | 123.76
Linear Model | 99.5314 | 101.7065 | 104.6067 | 107.5068 | 110.407 | 113.3071 | 116.2073 | 119.1074 | 122.0076
MICRO-54
16 active threads / warp:
Instruction 1
time
power
Notes: However, the linear static power model does not always match real-world observations.
When we measure the power of a microbenchmark on real silicon that issues integer multiply operations with varying threads per warp, we observe significant deviation from the linear model.
(next slide)
Volta has 4 processing blocks per SM and only 16 integer functional units per processing block.
Thus, a warp executes in half-warp steps.
(next slide)
If there are only 16 active threads in a warp, then the first 16 active-thread half-warp always executes, ...
(next slide)
...but the system forgoes the execution of the 2nd empty half-warp.
(next slide)
Thus, one full half-warp...
(next slide)
...executes after another.
(next slide)
Hence, the system runs at full int multiply utilization and reaches maximum power.
Similarly, when there are 32 active threads per warp, then both half-warps fully utilize functional units, and the system again reaches power close to the maximum.
(next slide)
If, however, we have 20 active threads, then the execution of full half-warps...
(next slide)
...is interleaved with mostly empty ones that have only 4 active threads.
(next slide)
...and this behavior...
(next slide)
...repeats.
(next slide)
Thus, the overall power consumption drops even though the energy consumption per warp instruction is higher.

## Slide 21: Divergence-Aware Static Power Model
Chart: INT_MUL
| 1 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32
Measured | 100.6108 | 101.8406 | 110.1956 | 118.91 | 127.56 | 113.74 | 117.355 | 120.468 | 123.76
Linear Model | 99.5314 | 101.7065 | 104.6067 | 107.5068 | 110.407 | 113.3071 | 116.2073 | 119.1074 | 122.0076
MICRO-54
16 active threads / warp:
Instruction 1
time
power
Notes: However, the linear static power model does not always match real-world observations.
When we measure the power of a microbenchmark on real silicon that issues integer multiply operations with varying threads per warp, we observe significant deviation from the linear model.
(next slide)
Volta has 4 processing blocks per SM and only 16 integer functional units per processing block.
Thus, a warp executes in half-warp steps.
(next slide)
If there are only 16 active threads in a warp, then the first 16 active-thread half-warp always executes, ...
(next slide)
...but the system forgoes the execution of the 2nd empty half-warp.
(next slide)
Thus, one full half-warp...
(next slide)
...executes after another.
(next slide)
Hence, the system runs at full int multiply utilization and reaches maximum power.
Similarly, when there are 32 active threads per warp, then both half-warps fully utilize functional units, and the system again reaches power close to the maximum.
(next slide)
If, however, we have 20 active threads, then the execution of full half-warps...
(next slide)
...is interleaved with mostly empty ones that have only 4 active threads.
(next slide)
...and this behavior...
(next slide)
...repeats.
(next slide)
Thus, the overall power consumption drops even though the energy consumption per warp instruction is higher.

## Slide 22: Divergence-Aware Static Power Model
Chart: INT_MUL
| 1 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32
Measured | 100.6108 | 101.8406 | 110.1956 | 118.91 | 127.56 | 113.74 | 117.355 | 120.468 | 123.76
Linear Model | 99.5314 | 101.7065 | 104.6067 | 107.5068 | 110.407 | 113.3071 | 116.2073 | 119.1074 | 122.0076
MICRO-54
16 active threads / warp:
Instruction 1
Instruction 2
time
power
Notes: However, the linear static power model does not always match real-world observations.
When we measure the power of a microbenchmark on real silicon that issues integer multiply operations with varying threads per warp, we observe significant deviation from the linear model.
(next slide)
Volta has 4 processing blocks per SM and only 16 integer functional units per processing block.
Thus, a warp executes in half-warp steps.
(next slide)
If there are only 16 active threads in a warp, then the first 16 active-thread half-warp always executes, ...
(next slide)
...but the system forgoes the execution of the 2nd empty half-warp.
(next slide)
Thus, one full half-warp...
(next slide)
...executes after another.
(next slide)
Hence, the system runs at full int multiply utilization and reaches maximum power.
Similarly, when there are 32 active threads per warp, then both half-warps fully utilize functional units, and the system again reaches power close to the maximum.
(next slide)
If, however, we have 20 active threads, then the execution of full half-warps...
(next slide)
...is interleaved with mostly empty ones that have only 4 active threads.
(next slide)
...and this behavior...
(next slide)
...repeats.
(next slide)
Thus, the overall power consumption drops even though the energy consumption per warp instruction is higher.

## Slide 23: Divergence-Aware Static Power Model
Chart: INT_MUL
| 1 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32
Measured | 100.6108 | 101.8406 | 110.1956 | 118.91 | 127.56 | 113.74 | 117.355 | 120.468 | 123.76
Linear Model | 99.5314 | 101.7065 | 104.6067 | 107.5068 | 110.407 | 113.3071 | 116.2073 | 119.1074 | 122.0076
MICRO-54
16 active threads / warp:
Instruction 1
Instruction 2
Instruction 3
time
power
Notes: However, the linear static power model does not always match real-world observations.
When we measure the power of a microbenchmark on real silicon that issues integer multiply operations with varying threads per warp, we observe significant deviation from the linear model.
(next slide)
Volta has 4 processing blocks per SM and only 16 integer functional units per processing block.
Thus, a warp executes in half-warp steps.
(next slide)
If there are only 16 active threads in a warp, then the first 16 active-thread half-warp always executes, ...
(next slide)
...but the system forgoes the execution of the 2nd empty half-warp.
(next slide)
Thus, one full half-warp...
(next slide)
...executes after another.
(next slide)
Hence, the system runs at full int multiply utilization and reaches maximum power.
Similarly, when there are 32 active threads per warp, then both half-warps fully utilize functional units, and the system again reaches power close to the maximum.
(next slide)
If, however, we have 20 active threads, then the execution of full half-warps...
(next slide)
...is interleaved with mostly empty ones that have only 4 active threads.
(next slide)
...and this behavior...
(next slide)
...repeats.
(next slide)
Thus, the overall power consumption drops even though the energy consumption per warp instruction is higher.

## Slide 24: Divergence-Aware Static Power Model
Chart: INT_MUL
| 1 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32
Measured | 100.6108 | 101.8406 | 110.1956 | 118.91 | 127.56 | 113.74 | 117.355 | 120.468 | 123.76
Linear Model | 99.5314 | 101.7065 | 104.6067 | 107.5068 | 110.407 | 113.3071 | 116.2073 | 119.1074 | 122.0076
MICRO-54
16 active threads / warp:
Instruction 1
Instruction 2
Instruction 3
time
power
Average power
Notes: However, the linear static power model does not always match real-world observations.
When we measure the power of a microbenchmark on real silicon that issues integer multiply operations with varying threads per warp, we observe significant deviation from the linear model.
(next slide)
Volta has 4 processing blocks per SM and only 16 integer functional units per processing block.
Thus, a warp executes in half-warp steps.
(next slide)
If there are only 16 active threads in a warp, then the first 16 active-thread half-warp always executes, ...
(next slide)
...but the system forgoes the execution of the 2nd empty half-warp.
(next slide)
Thus, one full half-warp...
(next slide)
...executes after another.
(next slide)
Hence, the system runs at full int multiply utilization and reaches maximum power.
Similarly, when there are 32 active threads per warp, then both half-warps fully utilize functional units, and the system again reaches power close to the maximum.
(next slide)
If, however, we have 20 active threads, then the execution of full half-warps...
(next slide)
...is interleaved with mostly empty ones that have only 4 active threads.
(next slide)
...and this behavior...
(next slide)
...repeats.
(next slide)
Thus, the overall power consumption drops even though the energy consumption per warp instruction is higher.

## Slide 25: Divergence-Aware Static Power Model
Chart: INT_MUL
| 1 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32
Measured | 100.6108 | 101.8406 | 110.1956 | 118.91 | 127.56 | 113.74 | 117.355 | 120.468 | 123.76
Linear Model | 99.5314 | 101.7065 | 104.6067 | 107.5068 | 110.407 | 113.3071 | 116.2073 | 119.1074 | 122.0076
MICRO-54
20 active threads / warp:
Instruction 1
time
power
Notes: However, the linear static power model does not always match real-world observations.
When we measure the power of a microbenchmark on real silicon that issues integer multiply operations with varying threads per warp, we observe significant deviation from the linear model.
(next slide)
Volta has 4 processing blocks per SM and only 16 integer functional units per processing block.
Thus, a warp executes in half-warp steps.
(next slide)
If there are only 16 active threads in a warp, then the first 16 active-thread half-warp always executes, ...
(next slide)
...but the system forgoes the execution of the 2nd empty half-warp.
(next slide)
Thus, one full half-warp...
(next slide)
...executes after another.
(next slide)
Hence, the system runs at full int multiply utilization and reaches maximum power.
Similarly, when there are 32 active threads per warp, then both half-warps fully utilize functional units, and the system again reaches power close to the maximum.
(next slide)
If, however, we have 20 active threads, then the execution of full half-warps...
(next slide)
...is interleaved with mostly empty ones that have only 4 active threads.
(next slide)
...and this behavior...
(next slide)
...repeats.
(next slide)
Thus, the overall power consumption drops even though the energy consumption per warp instruction is higher.

## Slide 26: Divergence-Aware Static Power Model
Chart: INT_MUL
| 1 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32
Measured | 100.6108 | 101.8406 | 110.1956 | 118.91 | 127.56 | 113.74 | 117.355 | 120.468 | 123.76
Linear Model | 99.5314 | 101.7065 | 104.6067 | 107.5068 | 110.407 | 113.3071 | 116.2073 | 119.1074 | 122.0076
MICRO-54
20 active threads / warp:
Instruction 1
time
power
Notes: However, the linear static power model does not always match real-world observations.
When we measure the power of a microbenchmark on real silicon that issues integer multiply operations with varying threads per warp, we observe significant deviation from the linear model.
(next slide)
Volta has 4 processing blocks per SM and only 16 integer functional units per processing block.
Thus, a warp executes in half-warp steps.
(next slide)
If there are only 16 active threads in a warp, then the first 16 active-thread half-warp always executes, ...
(next slide)
...but the system forgoes the execution of the 2nd empty half-warp.
(next slide)
Thus, one full half-warp...
(next slide)
...executes after another.
(next slide)
Hence, the system runs at full int multiply utilization and reaches maximum power.
Similarly, when there are 32 active threads per warp, then both half-warps fully utilize functional units, and the system again reaches power close to the maximum.
(next slide)
If, however, we have 20 active threads, then the execution of full half-warps...
(next slide)
...is interleaved with mostly empty ones that have only 4 active threads.
(next slide)
...and this behavior...
(next slide)
...repeats.
(next slide)
Thus, the overall power consumption drops even though the energy consumption per warp instruction is higher.

## Slide 27: Divergence-Aware Static Power Model
Chart: INT_MUL
| 1 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32
Measured | 100.6108 | 101.8406 | 110.1956 | 118.91 | 127.56 | 113.74 | 117.355 | 120.468 | 123.76
Linear Model | 99.5314 | 101.7065 | 104.6067 | 107.5068 | 110.407 | 113.3071 | 116.2073 | 119.1074 | 122.0076
MICRO-54
20 active threads / warp:
Instruction 1
time
power
Instruction 2
Notes: However, the linear static power model does not always match real-world observations.
When we measure the power of a microbenchmark on real silicon that issues integer multiply operations with varying threads per warp, we observe significant deviation from the linear model.
(next slide)
Volta has 4 processing blocks per SM and only 16 integer functional units per processing block.
Thus, a warp executes in half-warp steps.
(next slide)
If there are only 16 active threads in a warp, then the first 16 active-thread half-warp always executes, ...
(next slide)
...but the system forgoes the execution of the 2nd empty half-warp.
(next slide)
Thus, one full half-warp...
(next slide)
...executes after another.
(next slide)
Hence, the system runs at full int multiply utilization and reaches maximum power.
Similarly, when there are 32 active threads per warp, then both half-warps fully utilize functional units, and the system again reaches power close to the maximum.
(next slide)
If, however, we have 20 active threads, then the execution of full half-warps...
(next slide)
...is interleaved with mostly empty ones that have only 4 active threads.
(next slide)
...and this behavior...
(next slide)
...repeats.
(next slide)
Thus, the overall power consumption drops even though the energy consumption per warp instruction is higher.

## Slide 28: Divergence-Aware Static Power Model
Chart: INT_MUL
| 1 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32
Measured | 100.6108 | 101.8406 | 110.1956 | 118.91 | 127.56 | 113.74 | 117.355 | 120.468 | 123.76
Linear Model | 99.5314 | 101.7065 | 104.6067 | 107.5068 | 110.407 | 113.3071 | 116.2073 | 119.1074 | 122.0076
MICRO-54
20 active threads / warp:
Instruction 1
time
power
Instruction 2
Notes: However, the linear static power model does not always match real-world observations.
When we measure the power of a microbenchmark on real silicon that issues integer multiply operations with varying threads per warp, we observe significant deviation from the linear model.
(next slide)
Volta has 4 processing blocks per SM and only 16 integer functional units per processing block.
Thus, a warp executes in half-warp steps.
(next slide)
If there are only 16 active threads in a warp, then the first 16 active-thread half-warp always executes, ...
(next slide)
...but the system forgoes the execution of the 2nd empty half-warp.
(next slide)
Thus, one full half-warp...
(next slide)
...executes after another.
(next slide)
Hence, the system runs at full int multiply utilization and reaches maximum power.
Similarly, when there are 32 active threads per warp, then both half-warps fully utilize functional units, and the system again reaches power close to the maximum.
(next slide)
If, however, we have 20 active threads, then the execution of full half-warps...
(next slide)
...is interleaved with mostly empty ones that have only 4 active threads.
(next slide)
...and this behavior...
(next slide)
...repeats.
(next slide)
Thus, the overall power consumption drops even though the energy consumption per warp instruction is higher.

## Slide 29: Divergence-Aware Static Power Model
Chart: INT_MUL
| 1 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32
Measured | 100.6108 | 101.8406 | 110.1956 | 118.91 | 127.56 | 113.74 | 117.355 | 120.468 | 123.76
Linear Model | 99.5314 | 101.7065 | 104.6067 | 107.5068 | 110.407 | 113.3071 | 116.2073 | 119.1074 | 122.0076
MICRO-54
20 active threads / warp:
Instruction 1
time
power
Instruction 2
Average power
Notes: However, the linear static power model does not always match real-world observations.
When we measure the power of a microbenchmark on real silicon that issues integer multiply operations with varying threads per warp, we observe significant deviation from the linear model.
(next slide)
Volta has 4 processing blocks per SM and only 16 integer functional units per processing block.
Thus, a warp executes in half-warp steps.
(next slide)
If there are only 16 active threads in a warp, then the first 16 active-thread half-warp always executes, ...
(next slide)
...but the system forgoes the execution of the 2nd empty half-warp.
(next slide)
Thus, one full half-warp...
(next slide)
...executes after another.
(next slide)
Hence, the system runs at full int multiply utilization and reaches maximum power.
Similarly, when there are 32 active threads per warp, then both half-warps fully utilize functional units, and the system again reaches power close to the maximum.
(next slide)
If, however, we have 20 active threads, then the execution of full half-warps...
(next slide)
...is interleaved with mostly empty ones that have only 4 active threads.
(next slide)
...and this behavior...
(next slide)
...repeats.
(next slide)
Thus, the overall power consumption drops even though the energy consumption per warp instruction is higher.

## Slide 30: Divergence-Aware Static Power Model
Chart: INT_MUL
| 1 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32
Measured | 100.6108 | 101.8406 | 110.1956 | 118.91 | 127.56 | 113.74 | 117.355 | 120.468 | 123.76
Linear Model | 99.5314 | 101.7065 | 104.6067 | 107.5068 | 110.407 | 113.3071 | 116.2073 | 119.1074 | 122.0076
Half-warp Model | 99.5314 | 104.0267 | 110.0203 | 116.014 | 122.0076 | 113.0171 | 116.014 | 119.0108 | 122.0076
MICRO-54
Linear Model
Half-warp Model
Notes: We capture this saw-tooth behavior with our half-warp static power model.
The half-warp model closely tracks hardware power measurements.
//explain the equation?

## Slide 31: Accounting for Intra-warp Functional Unit Overlap
Chart: INT_MUL
| 1 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32
Measured | 100.6108 | 101.8406 | 110.1956 | 118.91 | 127.56 | 113.74 | 117.355 | 120.468 | 123.76
Linear Model | 99.5314 | 101.7065 | 104.6067 | 107.5068 | 110.407 | 113.3071 | 116.2073 | 119.1074 | 122.0076
Half-warp Model | 99.5314 | 104.0267 | 110.0203 | 116.014 | 122.0076 | 113.0171 | 116.014 | 119.0108 | 122.0076
Chart: INT_FP
| 1 | 8 | 16 | 24 | 32
Measured | 106.2436 | 124.3 | 151.57 | 157.215 | 169.1
Linear Model | 105.1866 | 118.6383 | 134.0117 | 149.385 | 164.7584
Half-warp Model | 105.1866 | 132.9868 | 164.7584 | 148.8726 | 164.7584
MICRO-54
Linear Model
Half-warp Model
Notes: However, when exercising two units by using microbenchmarks that issue both INT32 and FP32 instructions, the half-warp behavior is less pronounced. This is because Volta can simultaneously execute operations in the same processing block by running multiple functional units concurrently.
(Next Slide)
As instructions from the same thread that utilize the INT32 and FP32 units can execute concurrently within a processing block, ...
(Next Slide)
...the system exhibits a statistical mix of full and partial utilization...
(Next Slide)
... of these functional units within each SM
(Next Slide)
As a result, the average power does not drop as dramatically as when only one unit is utilized.

## Slide 32: Accounting for Intra-warp Functional Unit Overlap
Chart: INT_FP
| 1 | 8 | 16 | 24 | 32
Measured | 106.2436 | 124.3 | 151.57 | 157.215 | 169.1
Linear Model | 105.1866 | 118.6383 | 134.0117 | 149.385 | 164.7584
Half-warp Model | 105.1866 | 132.9868 | 164.7584 | 148.8726 | 164.7584
MICRO-54
int instruction
FP instruction
int + some FP
24 active threads / warp:
time
power
int + some FP
Notes: However, when exercising two units by using microbenchmarks that issue both INT32 and FP32 instructions, the half-warp behavior is less pronounced. This is because Volta can simultaneously execute operations in the same processing block by running multiple functional units concurrently.
(Next Slide)
As instructions from the same thread that utilize the INT32 and FP32 units can execute concurrently within a processing block, ...
(Next Slide)
...the system exhibits a statistical mix of full and partial utilization...
(Next Slide)
... of these functional units within each SM
(Next Slide)
As a result, the average power does not drop as dramatically as when only one unit is utilized.

## Slide 33: Accounting for Intra-warp Functional Unit Overlap
Chart: INT_FP
| 1 | 8 | 16 | 24 | 32
Measured | 106.2436 | 124.3 | 151.57 | 157.215 | 169.1
Linear Model | 105.1866 | 118.6383 | 134.0117 | 149.385 | 164.7584
Half-warp Model | 105.1866 | 132.9868 | 164.7584 | 148.8726 | 164.7584
MICRO-54
int instruction
FP instruction
FP + some int
24 active threads / warp:
time
power
int + some FP
FP + some int
Notes: However, when exercising two units by using microbenchmarks that issue both INT32 and FP32 instructions, the half-warp behavior is less pronounced. This is because Volta can simultaneously execute operations in the same processing block by running multiple functional units concurrently.
(Next Slide)
As instructions from the same thread that utilize the INT32 and FP32 units can execute concurrently within a processing block, ...
(Next Slide)
...the system exhibits a statistical mix of full and partial utilization...
(Next Slide)
... of these functional units within each SM
(Next Slide)
As a result, the average power does not drop as dramatically as when only one unit is utilized.

## Slide 34: Accounting for Intra-warp Functional Unit Overlap
Chart: INT_FP
| 1 | 8 | 16 | 24 | 32
Measured | 106.2436 | 124.3 | 151.57 | 157.215 | 169.1
Linear Model | 105.1866 | 118.6383 | 134.0117 | 149.385 | 164.7584
Half-warp Model | 105.1866 | 132.9868 | 164.7584 | 148.8726 | 164.7584
MICRO-54
FP instruction
int instr.
int + some FP
24 active threads / warp:
time
power
int + some FP
int + some FP
FP + some int
Notes: However, when exercising two units by using microbenchmarks that issue both INT32 and FP32 instructions, the half-warp behavior is less pronounced. This is because Volta can simultaneously execute operations in the same processing block by running multiple functional units concurrently.
(Next Slide)
As instructions from the same thread that utilize the INT32 and FP32 units can execute concurrently within a processing block, ...
(Next Slide)
...the system exhibits a statistical mix of full and partial utilization...
(Next Slide)
... of these functional units within each SM
(Next Slide)
As a result, the average power does not drop as dramatically as when only one unit is utilized.

## Slide 35: Accounting for Intra-warp Functional Unit Overlap
Chart: INT_FP
| 1 | 8 | 16 | 24 | 32
Measured | 106.2436 | 124.3 | 151.57 | 157.215 | 169.1
Linear Model | 105.1866 | 118.6383 | 134.0117 | 149.385 | 164.7584
Half-warp Model | 105.1866 | 132.9868 | 164.7584 | 148.8726 | 164.7584
MICRO-54
24 active threads / warp:
time
power
Average power
int + some FP
int + some FP
FP + some int
FP instruction
int instruction
FP instruction
int instr.
Notes: However, when exercising two units by using microbenchmarks that issue both INT32 and FP32 instructions, the half-warp behavior is less pronounced. This is because Volta can simultaneously execute operations in the same processing block by running multiple functional units concurrently.
(Next Slide)
As instructions from the same thread that utilize the INT32 and FP32 units can execute concurrently within a processing block, ...
(Next Slide)
...the system exhibits a statistical mix of full and partial utilization...
(Next Slide)
... of these functional units within each SM
(Next Slide)
As a result, the average power does not drop as dramatically as when only one unit is utilized.

## Slide 36: Accounting for Intra-warp Functional Unit Overlap
Chart: INT_MUL
| 1 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32
Measured | 100.6108 | 101.8406 | 110.1956 | 118.91 | 127.56 | 113.74 | 117.355 | 120.468 | 123.76
Linear Model | 99.5314 | 101.7065 | 104.6067 | 107.5068 | 110.407 | 113.3071 | 116.2073 | 119.1074 | 122.0076
Half-warp Model | 99.5314 | 104.0267 | 110.0203 | 116.014 | 122.0076 | 113.0171 | 116.014 | 119.0108 | 122.0076
Chart: INT_FP
| 1 | 8 | 16 | 24 | 32
Measured | 106.2436 | 124.3 | 151.57 | 157.215 | 169.1
Linear Model | 105.1866 | 118.6383 | 134.0117 | 149.385 | 164.7584
Half-warp Model | 105.1866 | 132.9868 | 164.7584 | 148.8726 | 164.7584
Chart: INT_FP_SFU
| 1 | 8 | 16 | 24 | 32
Measured | 114.6167 | 119.5433 | 129.5225 | 138.455 | 142.6
Linear Model | 111.6683 | 118.6508 | 126.6309 | 134.6109 | 142.591
Half-warp Model | 111.6683 | 126.0989 | 142.591 | 134.3449 | 142.591
MICRO-54
Linear Model
Half-warp Model
Notes: Thus, as ILP increases in the kernel, the more Functional units are executing simultaneously, and the power behavior transitions gradually from a half-warp behavior(point to INT_MUL), to a behavior between linear and half-warp (point to INT_FP) , to almost purely linear (point to INT_FP_SFU).
AccelWattch accounts for the effects of intra-warp functional unit execution overlap by monitoring the mix of executed instructions and picking the appropriate model.
To the best of our knowledge, AccelWattch is the first model that accounts for power-gating, the half-warp behaviour, and the intra-warp functional unit execution overlap.

## Slide 37: Accounting for Intra-warp Functional Unit Overlap
Chart: INT_MUL
| 1 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32
Measured | 100.6108 | 101.8406 | 110.1956 | 118.91 | 127.56 | 113.74 | 117.355 | 120.468 | 123.76
Linear Model | 99.5314 | 101.7065 | 104.6067 | 107.5068 | 110.407 | 113.3071 | 116.2073 | 119.1074 | 122.0076
Half-warp Model | 99.5314 | 104.0267 | 110.0203 | 116.014 | 122.0076 | 113.0171 | 116.014 | 119.0108 | 122.0076
Chart: INT_FP
| 1 | 8 | 16 | 24 | 32
Measured | 106.2436 | 124.3 | 151.57 | 157.215 | 169.1
Linear Model | 105.1866 | 118.6383 | 134.0117 | 149.385 | 164.7584
Half-warp Model | 105.1866 | 132.9868 | 164.7584 | 148.8726 | 164.7584
Chart: INT_FP_SFU
| 1 | 8 | 16 | 24 | 32
Measured | 114.6167 | 119.5433 | 129.5225 | 138.455 | 142.6
Linear Model | 111.6683 | 118.6508 | 126.6309 | 134.6109 | 142.591
Half-warp Model | 111.6683 | 126.0989 | 142.591 | 134.3449 | 142.591
MICRO-54
Linear Model
Half-warp Model
Notes: Thus, as ILP increases in the kernel, the more Functional units are executing simultaneously, and the power behavior transitions gradually from a half-warp behavior (point to INT_MUL), to a behavior between linear and half-warp (point to INT_FP) , to almost purely linear (point to INT_FP_SFU).
AccelWattch accounts for the effects of intra-warp functional unit execution overlap by monitoring the mix of executed instructions and picking the appropriate model.
To the best of our knowledge, AccelWattch is the first model that accounts for power-gating, the half-warp behaviour, and the intra-warp functional unit execution overlap.

## Slide 38: Accounting for Intra-warp Functional Unit Overlap
Chart: INT_MUL
| 1 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32
Measured | 100.6108 | 101.8406 | 110.1956 | 118.91 | 127.56 | 113.74 | 117.355 | 120.468 | 123.76
Linear Model | 99.5314 | 101.7065 | 104.6067 | 107.5068 | 110.407 | 113.3071 | 116.2073 | 119.1074 | 122.0076
Half-warp Model | 99.5314 | 104.0267 | 110.0203 | 116.014 | 122.0076 | 113.0171 | 116.014 | 119.0108 | 122.0076
Chart: INT_FP
| 1 | 8 | 16 | 24 | 32
Measured | 106.2436 | 124.3 | 151.57 | 157.215 | 169.1
Linear Model | 105.1866 | 118.6383 | 134.0117 | 149.385 | 164.7584
Half-warp Model | 105.1866 | 132.9868 | 164.7584 | 148.8726 | 164.7584
Chart: INT_FP_SFU
| 1 | 8 | 16 | 24 | 32
Measured | 114.6167 | 119.5433 | 129.5225 | 138.455 | 142.6
Linear Model | 111.6683 | 118.6508 | 126.6309 | 134.6109 | 142.591
Half-warp Model | 111.6683 | 126.0989 | 142.591 | 134.3449 | 142.591
MICRO-54
Linear Model
Half-warp Model
Notes: Thus, as ILP increases in the kernel, the more Functional units are executing simultaneously, and the power behavior transitions gradually from a half-warp behavior (point to INT_MUL), to a behavior between linear and half-warp (point to INT_FP) , to almost purely linear (point to INT_FP_SFU).
AccelWattch accounts for the effects of intra-warp functional unit execution overlap by monitoring the mix of executed instructions and picking the appropriate model.
To the best of our knowledge, AccelWattch is the first model that accounts for power-gating, the half-warp behavior, and the intra-warp functional unit execution overlap.

## Slide 39: Accounting for Intra-warp Functional Unit Overlap
Chart: INT_MUL
| 1 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32
Measured | 100.6108 | 101.8406 | 110.1956 | 118.91 | 127.56 | 113.74 | 117.355 | 120.468 | 123.76
Linear Model | 99.5314 | 101.7065 | 104.6067 | 107.5068 | 110.407 | 113.3071 | 116.2073 | 119.1074 | 122.0076
Half-warp Model | 99.5314 | 104.0267 | 110.0203 | 116.014 | 122.0076 | 113.0171 | 116.014 | 119.0108 | 122.0076
Chart: INT_FP
| 1 | 8 | 16 | 24 | 32
Measured | 106.2436 | 124.3 | 151.57 | 157.215 | 169.1
Linear Model | 105.1866 | 118.6383 | 134.0117 | 149.385 | 164.7584
Half-warp Model | 105.1866 | 132.9868 | 164.7584 | 148.8726 | 164.7584
Chart: INT_FP_SFU
| 1 | 8 | 16 | 24 | 32
Measured | 114.6167 | 119.5433 | 129.5225 | 138.455 | 142.6
Linear Model | 111.6683 | 118.6508 | 126.6309 | 134.6109 | 142.591
Half-warp Model | 111.6683 | 126.0989 | 142.591 | 134.3449 | 142.591
MICRO-54
Linear Model
Half-warp Model
Notes: Thus, as ILP increases in the kernel, the more Functional units are executing simultaneously, and the power behavior transitions gradually from a half-warp behavior (point to INT_MUL), to a behavior between linear and half-warp (point to INT_FP) , to almost purely linear (point to INT_FP_SFU).
AccelWattch accounts for the effects of intra-warp functional unit execution overlap by monitoring the mix of executed instructions and picking the appropriate model.
To the best of our knowledge, AccelWattch is the first model that accounts for power-gating, the half-warp behaviour, and the intra-warp functional unit execution overlap.

## Slide 40: Accounting for Intra-warp Functional Unit Overlap
Chart: INT_MUL
| 1 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32
Measured | 100.6108 | 101.8406 | 110.1956 | 118.91 | 127.56 | 113.74 | 117.355 | 120.468 | 123.76
Linear Model | 99.5314 | 101.7065 | 104.6067 | 107.5068 | 110.407 | 113.3071 | 116.2073 | 119.1074 | 122.0076
Half-warp Model | 99.5314 | 104.0267 | 110.0203 | 116.014 | 122.0076 | 113.0171 | 116.014 | 119.0108 | 122.0076
Chart: INT_FP
| 1 | 8 | 16 | 24 | 32
Measured | 106.2436 | 124.3 | 151.57 | 157.215 | 169.1
Linear Model | 105.1866 | 118.6383 | 134.0117 | 149.385 | 164.7584
Half-warp Model | 105.1866 | 132.9868 | 164.7584 | 148.8726 | 164.7584
Chart: INT_FP_SFU
| 1 | 8 | 16 | 24 | 32
Measured | 114.6167 | 119.5433 | 129.5225 | 138.455 | 142.6
Linear Model | 111.6683 | 118.6508 | 126.6309 | 134.6109 | 142.591
Half-warp Model | 111.6683 | 126.0989 | 142.591 | 134.3449 | 142.591
MICRO-54
Linear Model
Half-warp Model
Notes: Thus, as ILP increases in the kernel, the more Functional units are executing simultaneously, and the power behavior transitions gradually from a half-warp behavior (point to INT_MUL), to a behavior between linear and half-warp (point to INT_FP) , to almost purely linear (point to INT_FP_SFU).
AccelWattch accounts for the effects of intra-warp functional unit execution overlap by monitoring the mix of executed instructions and picking the appropriate model.
To the best of our knowledge, AccelWattch is the first model that accounts for power-gating, the half-warp behaviour, and the intra-warp functional unit execution overlap.

## Slide 41: Putting It All Together
MICRO-54
idleSM power
static power
Linear Model
Half-warp Model
Notes: Overall, we model total power by this equation where Pconst is the constant power,
Pstatic combines the half-warp and linear static power models,
And we also consider the nominal power consumed per idle SM.
Next, let’s look at our model for dynamic power.

## Slide 42: Microbenchmarking for Dynamic Power Model
MICRO-54
102 µBenchmarks
22 hardware components modeled
Hardware Component Category | AccelWattch Dynamic Power Components | µBench Count
Active/Idle SMs |  | 12
INT32 core | ALU, int mul/mad | 9
FP32 core | FPU, fp mul/mad | 8
FP64 core | DPU, dp mul/mad | 8
SFU | sqrt, log, sin/cos, exp | 9
Texture Unit | Texture Unit | 7
Register File | Register File | 1
dCaches+ Sh.Mem. + NoC | L1d, Shared Mem., Constant Cache, L2, NoC | 11
DRAM + MC | DRAM, Mem. Controller | 2
Tensor Core | Tensor Core | 6
Mix | all | 29
Other | L0i, L1i, Pipeline, Scheduler | 102
Notes: For dynamic, we consider 22 hardware components that contribute to dynamic power separately.
We created a suite of 102 microbenchmarks that stress these target hardware components to estimate their power consumption.
We group these microbenchmarks into different categories based on the hardware component they stress.
The mix category microbenchmarks target combinations of these categories.
The others category includes components such as the instruction caches that all microbenchmarks inevitably stress.
//Active/Idle SMs is a category that we tune separately through microbenchmarking; it does not participate in the quadratic programming solver process

## Slide 43: Microbenchmarking for Dynamic Power Model
MICRO-54
20%
0%
5%
10%
15%
Hardware Component Category | AccelWattch Dynamic Power Components | µBench Count
Active/Idle SMs |  | 12
INT32 core | ALU, int mul/mad | 9
FP32 core | FPU, fp mul/mad | 8
FP64 core | DPU, dp mul/mad | 8
SFU | sqrt, log, sin/cos, exp | 9
Texture Unit | Texture Unit | 7
Register File | Register File | 1
dCaches+ Sh.Mem. + NoC | L1d, Shared Mem., Constant Cache, L2, NoC | 11
DRAM + MC | DRAM, Mem. Controller | 2
Tensor Core | Tensor Core | 6
Mix | all | 29
Other | L0i, L1i, Pipeline, Scheduler | 102
102 µBenchmarks
22 hardware components modeled
Notes: The microbenchmarks successfully stress their target components as shown by the highlighted diagonal on the heatmap.
Each cell’s color in the heatmap encodes the fraction of dynamic power a microbenchmark consumes on the corresponding GPU component, as estimated by AccelWattch.
Some components like the register file or the components in the others category are stressed across all microbenchmarks.

## Slide 44: Dynamic Power Model Formulation
Collect for all 22 dynamic power components
Account for modeling inaccuracies with
MICRO-54
Component’s scaling factor
Component’s activity factor
Component’s initial estimate for energy per access
Notes: We formulate dynamic power as the sum of the power of each hardware component
For each dynamic power component we model, we collect an activity factor ‘a’ for the running kernel, which we multiply with the component’s estimated energy per access ‘E’ to calculate energy.
We account for any modeling inaccuracies with a scaling factor ‘x’ per component.

## Slide 45: Dynamic Power Model Formulation
Collect for all 22 dynamic power components
Account for modeling inaccuracies with
Use Quadratic Programming to tune (solve a 102×22 set of linear equations)
MICRO-54
Component’s scaling factor
Component’s activity factor
Component’s initial estimate for energy per access
Notes: We then formulate the dynamic power estimation task as a quadratic programming problem that tunes individual ‘x’ scaling factors to minimize the relative error between the modeled system power and the measured hardware power.
We obtain new per-component scaling factors that we supply to AccelWattch and re-iterate until the quadratic programming solver can no longer reduce the relative errors.
We enforce per-scaling-factor constraints on the quadratic solver to guard against unrealistic component power estimates.

## Slide 46: Where To Collect Activity Factors From?
MICRO-54
Simulation
  AccelWattch SASS SIM  Native ISA perf. simulation
  AccelWattch PTX SIM  Virtual ISA perf. simulation
Notes: So where can we collect these activity factors from?
Similar to previous power models, AccelWattch can rely on simulations to collect these activity factors.
We call these models AccelWattch SASS SIM and AccelWattch PTX SIM depending on the ISA level of performance simulations.

## Slide 47: Where To Collect Activity Factors From?
MICRO-54
Simulation
  AccelWattch SASS SIM  Native ISA perf. simulation
  AccelWattch PTX SIM  Virtual ISA perf. simulation
Hardware performance counters
  AccelWattch HW  Real hardware, no perf. simulation
Notes: Unlike previous models, AccelWattch can also be driven entirely by hardware performance counters derived from execution on real silicon.
We call this model AccelWattch HW.

## Slide 48: Where To Collect Activity Factors From?
MICRO-54
Simulation
  AccelWattch SASS SIM  Native ISA perf. simulation
  AccelWattch PTX SIM  Virtual ISA perf. simulation
Hardware performance counters
  AccelWattch HW  Real hardware, no perf. simulation
Mix of hardware performance counters + simulation
  AccelWattch HYBRID  Only individual component from perf. simulation
Notes: Furthermore, AccelWattch can be driven by a combination of activity factors collected from hardware performance counters and software performance simulations.
We call this model AccelWattch HYBRID
With AccelWattch HYBRID, users can partially avoid the inordinate amount of effort required to build, tune, and validate sophisticated software models of entire GPU architectures, and instead build models for only the few components that are relevant to their research.
They can then use hardware performance counters for all other components to estimate their system’s power with AccelWattch HYBRID.
To the best of our knowledge, AccelWattch is the first power model to afford such flexibility to its users, and allow trade offs in modeling accuracy vs. performance modeling effort and flexibility in which components to simulate.

## Slide 49: Methodology
GPUs
  Volta: Quadro GV100 @ 1417MHz
  Pascal: TITAN X @ 1470 MHz
  Turing: RTX 2060S @ 1905MHz
26 kernels from 18 workloads
  NVIDIA CUDA Samples 11.0
  Rodinia 3.1
  Parboil
  CUTLASS 1.3
DeepBench (6 workloads)
Activity factor collection:
  AccelWattch SASS SIM & PTX SIM: performance sim. (Accel-Sim v1.1)
  AccelWattch HW: hardware performance counters (NVIDIA Nsight Compute)
  AccelWattch HYBRID: {L2, NoC} from Accel-Sim rest from NVIDIA Nsight Compute
Hardware power measurements collected @ 65℃ from NVML
MAPE: Mean absolute percent error
MICRO-54
Notes: We validate AccelWattch against a Quadro GV100 GPU by applying the power model on a suite of 26 validation kernels obtained from NVIDIA CUDA samples, Rodinia, Parboil, and CUTLASS benchmark suites. We also apply AccelWattch for 6 DeepBench workloads.
Additionally, we validate AccelWattch against a Pascal TITAN X and a Turing RTX 2060 Super as part of a case study we will talk about later.
We use Accel-Sim for PTX and SASS performance simulations, and NVIDIA Nsight Compute for hardware performance counter collection.
The AccelWattch HYBRID configuration we validate here is with activity factors for the L2 Cache and Network-on-chip obtained from Accel-Sim simulations and the rest from hardware performance counters.
We collect all our hardware power measurements using NVML when the chip is at 65 degree Celsius. This is done to eliminate the effect of temperature variability on static power.
The metric we use to quantify accuracy is MAPE, mean absolute percent error.

## Slide 50: AccelWattch HW Closely Tracks HW Measurements
MICRO-54
AccelWattch HW, MAPE: 7.5%
Chart: Measured Power (W)
| 172.69880000000001 | 156.97620000000001 | 219.7978 | 152.1182 | 169.6574 | 111.86036 | 130.0522 | 121.5072 | 167.12520000000001 | 194.54820000000001 | 229.55340000000001 | 151.86259999999999 | 172.8844 | 201.33680000000001 | 189.4032 | 142.4556 | 217.49260000000001 | 153.00640000000001 | 145.70959999999999 | 200.44399999999999 | 188.54500000000002 | 181.99199999999999 | 101.92142 | 121.6066 | 177.99639999999999
 | 154.318 | 137.2427 | 208.7686 | 157.4801 | 172.0908 | 112.6452 | 124.8214 | 139.9703 | 192.501 | 191.2104 | 237.7753 | 158.1985 | 200.9502 | 226.3787 | 199.7925 | 124.7896 | 202.6408 | 151.3537 | 137.6918 | 209.7912 | 186.3381 | 162.1356 | 99.5574 | 132.1392 | 215.3407
 | 0 | 270
Notes: We tune AccelWattch using our microbenchmark suite on a Volta GPU, and then use the tuned model to estimate the total power consumption of our 26 kernels from our validation suite;
AccelWattch has not been tuned for these validation workloads.
AccelWattch HW correlates very well with hardware power measurements and achieves a MAPE of 7.5%.

## Slide 51: AccelWattch HYBRID Trades Off Accuracy for Flexibility
MICRO-54
AccelWattch HW, MAPE: 7.5%
AccelWattch HYBRID, MAPE: 8.2%
Chart: Measured Power (W)
| 172.69880000000001 | 156.97620000000001 | 219.7978 | 152.1182 | 169.6574 | 181.99199999999999 | 101.92142 | 121.6066 | 177.99639999999999 | 111.86036 | 130.0522 | 121.5072 | 167.12520000000001 | 194.54820000000001 | 229.55340000000001 | 151.86259999999999 | 172.8844 | 201.33680000000001 | 189.4032 | 142.4556 | 217.49260000000001 | 153.00640000000001 | 145.70959999999999 | 200.44399999999999 | 188.54500000000002
 | 151.1689 | 134.8206 | 207.1369 | 148.7279 | 168.2464 | 162.9115 | 99.5655 | 131.2838 | 217.137 | 102.8798 | 124.1757 | 131.4094 | 193.3037 | 190.9377 | 237.5056 | 136.9095 | 195.9356 | 235.0289 | 181.4468 | 123.8893 | 198.8883 | 152.4234 | 131.2649 | 206.241 | 178.9581
 | 0 | 270
Chart: Measured Power (W)
| 172.69880000000001 | 156.97620000000001 | 219.7978 | 152.1182 | 169.6574 | 111.86036 | 130.0522 | 121.5072 | 167.12520000000001 | 194.54820000000001 | 229.55340000000001 | 151.86259999999999 | 172.8844 | 201.33680000000001 | 189.4032 | 142.4556 | 217.49260000000001 | 153.00640000000001 | 145.70959999999999 | 200.44399999999999 | 188.54500000000002 | 181.99199999999999 | 101.92142 | 121.6066 | 177.99639999999999
 | 154.318 | 137.2427 | 208.7686 | 157.4801 | 172.0908 | 112.6452 | 124.8214 | 139.9703 | 192.501 | 191.2104 | 237.7753 | 158.1985 | 200.9502 | 226.3787 | 199.7925 | 124.7896 | 202.6408 | 151.3537 | 137.6918 | 209.7912 | 186.3381 | 162.1356 | 99.5574 | 132.1392 | 215.3407
 | 0 | 270
Notes: AccelWattch HYBRID trades off some of that accuracy for the flexibility to model a component in software and achieves a MAPE of 8.2%

## Slide 52: AccelWattch SASS SIM Offers Highest Flexibility
MICRO-54
AccelWattch HW, MAPE: 7.5%
AccelWattch HYBRID, MAPE: 8.2%
AccelWattch SASS SIM, MAPE: 9.2%
Chart: Measured Power (W)
| 172.69880000000001 | 156.97620000000001 | 219.7978 | 152.1182 | 169.6574 | 181.99199999999999 | 101.92142 | 121.6066 | 177.99639999999999 | 111.86036 | 130.0522 | 121.5072 | 167.12520000000001 | 194.54820000000001 | 229.55340000000001 | 151.86259999999999 | 172.8844 | 201.33680000000001 | 189.4032 | 142.4556 | 217.49260000000001 | 153.00640000000001 | 145.70959999999999 | 200.44399999999999 | 188.54500000000002
 | 151.1689 | 134.8206 | 207.1369 | 148.7279 | 168.2464 | 162.9115 | 99.5655 | 131.2838 | 217.137 | 102.8798 | 124.1757 | 131.4094 | 193.3037 | 190.9377 | 237.5056 | 136.9095 | 195.9356 | 235.0289 | 181.4468 | 123.8893 | 198.8883 | 152.4234 | 131.2649 | 206.241 | 178.9581
 | 0 | 270
Chart: Measured Power (W)
| 172.69880000000001 | 156.97620000000001 | 219.7978 | 152.1182 | 169.6574 | 181.99199999999999 | 101.92142 | 121.6066 | 177.99639999999999 | 111.86036 | 130.0522 | 121.5072 | 167.12520000000001 | 194.54820000000001 | 229.55340000000001 | 151.86259999999999 | 172.8844 | 201.33680000000001 | 189.4032 | 142.4556 | 217.49260000000001 | 152.56379999999999 | 153.00640000000001 | 145.70959999999999 | 200.44399999999999 | 188.54500000000002
 | 168.7029 | 151.6421 | 158.8679 | 155.4743 | 173.1113 | 203.8046 | 97.5294 | 126.1396 | 216.9814 | 100.5604 | 91.0525 | 130.319 | 196.2287 | 200.9178 | 221.7398 | 166.7775 | 194.3882 | 198.8917 | 179.4013 | 152.1026 | 211.7455 | 185.4898 | 165.6157 | 147.2966 | 228.2153 | 177.3867
 | 0 | 270
Chart: Measured Power (W)
| 172.69880000000001 | 156.97620000000001 | 219.7978 | 152.1182 | 169.6574 | 111.86036 | 130.0522 | 121.5072 | 167.12520000000001 | 194.54820000000001 | 229.55340000000001 | 151.86259999999999 | 172.8844 | 201.33680000000001 | 189.4032 | 142.4556 | 217.49260000000001 | 153.00640000000001 | 145.70959999999999 | 200.44399999999999 | 188.54500000000002 | 181.99199999999999 | 101.92142 | 121.6066 | 177.99639999999999
 | 154.318 | 137.2427 | 208.7686 | 157.4801 | 172.0908 | 112.6452 | 124.8214 | 139.9703 | 192.501 | 191.2104 | 237.7753 | 158.1985 | 200.9502 | 226.3787 | 199.7925 | 124.7896 | 202.6408 | 151.3537 | 137.6918 | 209.7912 | 186.3381 | 162.1356 | 99.5574 | 132.1392 | 215.3407
 | 0 | 270
Notes: Full GPU simulations in SASS gives the highest modeling flexibility but at the cost of accuracy. AccelWattch SASS SIM achieves a MAPE of 9.2%.

## Slide 53: Accuracy Performance Model Correlation to Silicon
MICRO-54
AccelWattch HW, MAPE: 7.5%
AccelWattch HYBRID, MAPE: 8.2%
AccelWattch SASS SIM, MAPE: 9.2%
AccelWattch PTX SIM, MAPE: 13.7%
Chart: Measured Power (W)
| 172.69880000000001 | 156.97620000000001 | 219.7978 | 152.1182 | 169.6574 | 181.99199999999999 | 101.92142 | 121.6066 | 177.99639999999999 | 111.86036 | 130.0522 | 121.5072 | 167.12520000000001 | 194.54820000000001 | 229.55340000000001 | 151.86259999999999 | 172.8844 | 201.33680000000001 | 189.4032 | 142.4556 | 217.49260000000001 | 153.00640000000001 | 145.70959999999999 | 200.44399999999999 | 188.54500000000002
 | 151.1689 | 134.8206 | 207.1369 | 148.7279 | 168.2464 | 162.9115 | 99.5655 | 131.2838 | 217.137 | 102.8798 | 124.1757 | 131.4094 | 193.3037 | 190.9377 | 237.5056 | 136.9095 | 195.9356 | 235.0289 | 181.4468 | 123.8893 | 198.8883 | 152.4234 | 131.2649 | 206.241 | 178.9581
 | 0 | 270
Chart: Measured Power (W)
| 172.69880000000001 | 156.97620000000001 | 219.7978 | 152.1182 | 169.6574 | 181.99199999999999 | 101.92142 | 121.6066 | 177.99639999999999 | 111.86036 | 130.0522 | 121.5072 | 167.12520000000001 | 194.54820000000001 | 229.55340000000001 | 151.86259999999999 | 172.8844 | 201.33680000000001 | 189.4032 | 142.4556 | 217.49260000000001 | 152.56379999999999 | 153.00640000000001 | 145.70959999999999 | 200.44399999999999 | 188.54500000000002
 | 168.7029 | 151.6421 | 158.8679 | 155.4743 | 173.1113 | 203.8046 | 97.5294 | 126.1396 | 216.9814 | 100.5604 | 91.0525 | 130.319 | 196.2287 | 200.9178 | 221.7398 | 166.7775 | 194.3882 | 198.8917 | 179.4013 | 152.1026 | 211.7455 | 185.4898 | 165.6157 | 147.2966 | 228.2153 | 177.3867
 | 0 | 270
Chart: Measured Power (W)
| 172.69880000000001 | 156.97620000000001 | 219.7978 | 152.1182 | 169.6574 | 181.99199999999999 | 111.86036 | 130.0522 | 121.5072 | 167.12520000000001 | 194.54820000000001 | 151.86259999999999 | 172.8844 | 201.33680000000001 | 189.4032 | 142.4556 | 217.49260000000001 | 153.00640000000001 | 145.70959999999999 | 200.44399999999999 | 188.54500000000002
 | 151.4969 | 144.5911 | 210.3321 | 168.0391 | 171.3856 | 136.6085 | 119.1921 | 90.9172 | 137.0282 | 214.1829 | 216.7937 | 148.656 | 183.5776 | 195.079 | 219.2281 | 122.0385 | 162.7708 | 204.3352 | 147.4421 | 256.5548 | 174.6333
 | 0 | 270
Chart: Measured Power (W)
| 172.69880000000001 | 156.97620000000001 | 219.7978 | 152.1182 | 169.6574 | 111.86036 | 130.0522 | 121.5072 | 167.12520000000001 | 194.54820000000001 | 229.55340000000001 | 151.86259999999999 | 172.8844 | 201.33680000000001 | 189.4032 | 142.4556 | 217.49260000000001 | 153.00640000000001 | 145.70959999999999 | 200.44399999999999 | 188.54500000000002 | 181.99199999999999 | 101.92142 | 121.6066 | 177.99639999999999
 | 154.318 | 137.2427 | 208.7686 | 157.4801 | 172.0908 | 112.6452 | 124.8214 | 139.9703 | 192.501 | 191.2104 | 237.7753 | 158.1985 | 200.9502 | 226.3787 | 199.7925 | 124.7896 | 202.6408 | 151.3537 | 137.6918 | 209.7912 | 186.3381 | 162.1356 | 99.5574 | 132.1392 | 215.3407
 | 0 | 270
Notes: PTX, being a virtual ISA, has no 1-1 correspondence to the instructions executing on hardware. Thus, AccelWattch PTX SIM shows a MAPE of 13.7%, which is the worst among all AccelWattch models.
Overall, we see that the accuracy of AccelWattch improves as the performance model gets closer to real silicon.

## Slide 54: AccelWattch is Accurate for DeepBench Workloads
MICRO-54
Chart: Measured Power (W)
| 177.18 | 170.46 | 143.98169999999999 | 149.04 | 69.38 | 85.33
conv-train conv-inference gemm-train gemm-inference rnn-lstm-train rnn-lstm-inference | 236.3744 | 152.372 | 144.279 | 149.6282 | 88.5167 | 89.2144
 | 0 | 260
DeepBench kernels  closed-source with hand-tuned SASS
AccelWattch SASS SIM achieves 12.8% MAPE for DeepBench
Notes: We also applied AccelWattch on workloads from DeepBench, a popular deep learning suite.
DeepBench uses closed-source hand-tuned kernels that have no PTX representations.
We treat the DeepBench workloads as a special case due to significant challenges in validating them.
AccelWattch SASS SIM achieves a 12.8% MAPE for these DeepBench workloads.
It is important to note that these validation challenges, and not AccelWattch inaccuracies, are responsible for the higher error we see.

## Slide 55: Typical Architectural Evaluation Workflow
MICRO-54
Use cases for AccelWattch
  Baseline & target designs  Volta, Pascal, Turing
Baseline Arch.
Target Arch.
http://clipart-library.com/ clipart/1836200.htm
Nvidia Volta
Nvidia Turing
Notes: To further evaluate accelwattch, we construct use cases that replicate common practices in computer architecture studies.
The common practice when evaluating a new architectural design is to start with a baseline, collect measurements across a wide range of workloads and then similarly collect measurements of the new design and normalize them against the baseline. In typical architectural studies, researchers consider average behaviour of their target design relative to the baseline across a wide range of workloads, not just a few special cases.
In line with this common practice, we envision a typical use of AccelWattch where a researcher starts with the Volta AccelWattch model as a baseline and attempts to predict the power consumption of another design with different architectural parameters.
Ideally, Volta chips with these different architectural parameters would exist so that we can validate against them, but that is not the case.
As a proxy for the use cases of AccelWattch, we pick the two architectures closest to Volta: that is, Pascal & Turing.
This is done because there is real HW to validate against and it is more likely that HW units are implemented similarly to Volta in these architectures.

## Slide 56: AccelWattch Enables Design Space Exploration
MICRO-54
Comparing across architectures
   AccelWattch estimates closely track hardware measurements
Chart: Avg. Relative Power
| Pascal (rel. to Volta) | Turing (rel. to Pascal) | Turing (rel. to Volta)
Modeled | -0.26937 | 0.25613 | -0.082292
Measured | -0.25647 | 0.26626 | -0.05231
Notes: Considering one of the architectures as a baseline and the other as the hypothetical target design, we show the estimated power of Pascal relative to the estimated power of Volta on average across our workloads. For validation purposes, we also show the average hardware measurement of Pascal relative to Volta.
As additional use cases, we show the same for Turing relative to Pascal and Turing relative to Volta.
We see that average AccelWattch estimations closely match relative hardware power measurements.
The errors range between 1-3%.
Thus, we show that AccelWattch can be applied successfully for design space exploration studies.

## Slide 57: AccelWattch Enables Design Space Exploration
MICRO-54
Comparing across architectures
   AccelWattch estimates closely track hardware measurements
Chart: Avg. Relative Power
| Pascal (rel. to Volta) | Turing (rel. to Pascal) | Turing (rel. to Volta)
Modeled | -0.26937 | 0.25613 | -0.082292
Measured | -0.25647 | 0.26626 | -0.05231
Notes: Considering one of the architectures as a baseline and the other as the hypothetical target design, we show the estimated power of Pascal relative to the estimated power of Volta on average across our workloads. For validation purposes, we also show the average hardware measurement of Pascal relative to Volta.
As additional use cases, we show the same for Turing relative to Pascal and Turing relative to Volta.
We see that average AccelWattch estimations closely match relative hardware power measurements.
The errors range between 1-3%.
Thus, we show that AccelWattch can be applied successfully for design space exploration studies.

## Slide 58: AccelWattch Enables Design Space Exploration
MICRO-54
Comparing across architectures
   AccelWattch estimates closely track hardware measurements
Chart: Avg. Relative Power
| Pascal (rel. to Volta) | Turing (rel. to Pascal) | Turing (rel. to Volta)
Modeled | -0.26937 | 0.25613 | -0.082292
Measured | -0.25647 | 0.26626 | -0.05231
Notes: Considering one of the architectures as a baseline and the other as the hypothetical target design, we show the estimated power of Pascal relative to the estimated power of Volta on average across our workloads. For validation purposes, we also show the average hardware measurement of Pascal relative to Volta.
As additional use cases, we show the same for Turing relative to Pascal and Turing relative to Volta.
We see that average AccelWattch estimations closely match relative hardware power measurements.
The errors range between 1-3%.
Thus, we show that AccelWattch can be applied successfully for design space exploration studies.

## Slide 59: AccelWattch Enables Design Space Exploration
MICRO-54
Comparing across architectures
   AccelWattch estimates closely track hardware measurements
Chart: Avg. Relative Power
| Pascal (rel. to Volta) | Turing (rel. to Pascal) | Turing (rel. to Volta)
Modeled | -0.26937 | 0.25613 | -0.082292
Measured | -0.25647 | 0.26626 | -0.05231
Notes: Considering one of the architectures as a baseline and the other as the hypothetical target design, we show the estimated power of Pascal relative to the estimated power of Volta on average across our workloads. For validation purposes, we also show the average hardware measurement of Pascal relative to Volta.
As additional use cases, we show the same for Turing relative to Pascal and Turing relative to Volta.
We see that average AccelWattch estimations closely match relative hardware power measurements.
The errors range between 1-3%.
Thus, we show that AccelWattch can be applied successfully for design space exploration studies.

## Slide 60: AccelWattch Enables Design Space Exploration
MICRO-54
Comparing across architectures
   AccelWattch estimates closely track hardware measurements
Chart: Avg. Relative Power
| Pascal (rel. to Volta) | Turing (rel. to Pascal) | Turing (rel. to Volta)
Modeled | -0.26937 | 0.25613 | -0.082292
Measured | -0.25647 | 0.26626 | -0.05231
Notes: Considering one of the architectures as a baseline and the other as the hypothetical target design, we show the estimated power of Pascal relative to the estimated power of Volta on average across our workloads. For validation purposes, we also show the average hardware measurement of Pascal relative to Volta.
As additional use cases, we show the same for Turing relative to Pascal and Turing relative to Volta.
We see that average AccelWattch estimations closely match relative hardware power measurements.
The errors range between 1-3%.
Thus, we show that AccelWattch can be applied successfully for design space exploration studies.

## Slide 61: AccelWattch is Publicly Available
MICRO-54
AccelWattch artifact
  Archived at https://doi.org/10.5281/zenodo.5398781
  AccelWattch & µBenchmarks source code, pre-compiled binaries, instruction traces, processing/job control scripts
  Reproduces key validation plots
Integration into official Accel-Sim GitHub repository soon!
  https://github.com/accel-sim/accel-sim-framework
Official release of AccelWattch V1.0 soon!
Notes: We publicly release AccelWattch along with the microbenchmarks source code, pre-compiled binaries, SASS instruction traces, and scripts to build, run and validate AccelWattch to reproduce the key validation figures.
To ease the adoption of our tool, we are also in the process of integrating AccelWattch with the latest version of Accel-Sim in the official Accel-Sim GitHub repository.

## Slide 62: Conclusions
MICRO-54
AccelWattch: a cycle-level power model for modern GPUs
  Accounts for DVFS, thread divergence, power gating, intra-warp functional unit overlap
  Driven by software perf. simulators, or hardware perf. counters, or both
    Allows trade offs in accuracy vs. modeling flexibility and effort
Highly accurate
  Achieves 7.5 – 9.2% MAPE vs. hardware measurements on GV100
Enables reliable design space exploration
  1 – 3% avg. error in relative power estimates (Turing & Pascal relative to Volta)
AccelWattch is publicly available at https://doi.org/10.5281/zenodo.5398781
Notes: In conclusion,
We introduce AccelWattch, a cycle-level power model for Modern GPUs that accounts for DVFS, thread divergence, power gating, intra-warp functional unit overlap, and variable SM occupancy.
AccelWattch can be driven by software performance simulations or by hardware performance counters or by a combination of both.
We show that AccelWattch successfully allows trade offs in accuracy vs. modeling flexibility and modeling effort.
AccelWattch is highly accurate with a 7.5 – 9.2% MAPE vs. hardware measurements on Volta.
We also show that AccelWattch enables reliable design space exploration with a 1-3% average error in relative power estimates between Turing, Pascal and Volta architectures.
The entire AccelWattch framework is publicly available.

## Slide 63: Thank You!
MICRO-54
This presentation and recording belong to the authors. No distribution is allowed without the authors’ permission.
Contact us: vijayk@u.northwestern.edu
See you there!
MICRO-54 Session 6B, Wednesday, October 20, 2021
Notes: Thank you for listening and I hope to see you at MICRO Session 6B if you have any questions.

## Slide 64: Backup Slides

## Slide 65: Why Not GPUWattch for Modern GPUs?
No detailed model to capture power gating
Methodology does not account for DVFS
MICRO-54

## Slide 66: Why Not GPUWattch for Modern GPUs?
No detailed model to capture power gating
   Static Power lumped into single constant
Methodology does not account for DVFS
   Unreliable estimation of Static + Constant Power ()
MICRO-54
Dynamic Power
Static Power

## Slide 67: Why Not GPUWattch for Modern GPUs?
Methodology does not account for DVFS
   Unreliable estimation of Static + Constant Power ()
MICRO-54
Dynamic Power
Static Power
Chart: Processor Frequency (GHz)
| 0.13500000000000001 | 0.20200000000000001 | 0.35199999999999998 | 0.502 | 0.65200000000000002 | 0.80200000000000005 | 1.0049999999999999 | 1.1020000000000001 | 1.2 | 1.35 | 1.4470000000000001
MIX | 38.7333 | 38.7933 | 45.3025 | 68.5 | 81.9467 | 91.6769 | 121.922 | 140.24 | 162.15 | 203.69 | 239.43
INT_ADD | 35.1367 | 35.28 | 37.96 | 47.87 | 53.492 | 60.5875 | 73.3125 | 81.589 | 99.2683 | 111.6017 | 129.9225
FP_ADD | 35.01 | 35.035 | 37.77 | 48.0675 | 51.558 | 56.1533 | 69.68 | 77.0206 | 88.104 | 106.584 | 121.612
FP_MUL | 34.6833 | 34.9767 | 37.8 | 47.0425 | 53.148 | 58.8733 | 70.0433 | 77.8115 | 86.8636 | 105.327 | 122.418
NANOSLEEP | 32.715 | 32.77 | 33.3833 | 35.0367 | 36.03 | 37.1967 | 41.32 | 43.7267 | 46.37 | 52.5475 | 56.94
Modeled | 27.2449 | 29.5338 | 30.6698 | 33.2131 | 35.7565 | 38.2998 | 40.8431 | 44.285 | 45.9297 | 47.5913 | 50.1346 | 51.7792
MIX model | -1.4502 | 17.8121 | 27.3718 | 48.7744 | 70.1769 | 91.5794 | 112.9819 | 141.9466 | 155.7869 | 169.7699 | 191.1724 | 205.0127
INT_ADD model | 15.4357 | 24.6357 | 29.2016 | 39.4238 | 49.646 | 59.8682 | 70.0905 | 83.9245 | 90.5349 | 97.2134 | 107.4356 | 114.046
FP_ADD model | 17.2311 | 25.518 | 29.6307 | 38.8384 | 48.0461 | 57.2537 | 66.4614 | 78.9225 | 84.8767 | 90.8924 | 100.1001 | 106.0544
FP_MUL model | 17.4589 | 25.744 | 29.8559 | 39.0616 | 48.2674 | 57.4731 | 66.6789 | 79.1373 | 85.0903 | 91.1047 | 100.3105 | 106.2635
-2W?
27W?
15W?

## Slide 68: Why Not GPUWattch for Modern GPUs?
Chart: Processor Frequency (GHz)
| 0.13500000000000001 | 0.20200000000000001 | 0.35199999999999998 | 0.502 | 0.65200000000000002 | 0.80200000000000005 | 1.0049999999999999 | 1.1020000000000001 | 1.2 | 1.35 | 1.4470000000000001
MIX | 38.7333 | 38.7933 | 45.3025 | 68.5 | 81.9467 | 91.6769 | 121.922 | 140.24 | 162.15 | 203.69 | 239.43
INT_ADD | 35.1367 | 35.28 | 37.96 | 47.87 | 53.492 | 60.5875 | 73.3125 | 81.589 | 99.2683 | 111.6017 | 129.9225
FP_ADD | 35.01 | 35.035 | 37.77 | 48.0675 | 51.558 | 56.1533 | 69.68 | 77.0206 | 88.104 | 106.584 | 121.612
FP_MUL | 34.6833 | 34.9767 | 37.8 | 47.0425 | 53.148 | 58.8733 | 70.0433 | 77.8115 | 86.8636 | 105.327 | 122.418
NANOSLEEP | 32.715 | 32.77 | 33.3833 | 35.0367 | 36.03 | 37.1967 | 41.32 | 43.7267 | 46.37 | 52.5475 | 56.94
Modeled | 27.2449 | 29.5338 | 30.6698 | 33.2131 | 35.7565 | 38.2998 | 40.8431 | 44.285 | 45.9297 | 47.5913 | 50.1346 | 51.7792
MIX model | -1.4502 | 17.8121 | 27.3718 | 48.7744 | 70.1769 | 91.5794 | 112.9819 | 141.9466 | 155.7869 | 169.7699 | 191.1724 | 205.0127
INT_ADD model | 15.4357 | 24.6357 | 29.2016 | 39.4238 | 49.646 | 59.8682 | 70.0905 | 83.9245 | 90.5349 | 97.2134 | 107.4356 | 114.046
FP_ADD model | 17.2311 | 25.518 | 29.6307 | 38.8384 | 48.0461 | 57.2537 | 66.4614 | 78.9225 | 84.8767 | 90.8924 | 100.1001 | 106.0544
FP_MUL model | 17.4589 | 25.744 | 29.8559 | 39.0616 | 48.2674 | 57.4731 | 66.6789 | 79.1373 | 85.0903 | 91.1047 | 100.3105 | 106.2635
Methodology does not account for DVFS
   Unreliable estimation of Static + Constant Power ()
MICRO-54
Does not work for modern GPUs!
-2W?
27W?
15W?
Dynamic Power
Static Power

## Slide 69: Quadratic Programming Formulation
MICRO-54
Scaling factor constraints
  Prevent them from growing too big or too small
  Enforce “expected” power inequalities

## Slide 70: AccelWattch Enables Design Space Exploration
MICRO-54
Pascal SASS SIM, MAPE: 11%
Turing SASS SIM, MAPE: 13%
Pascal PTX SIM, MAPE: 10.8%
Turing PTX SIM, MAPE: 14%
Chart: Measured Power (W)
| 108.2825 | 101.10499999999999 | 137.13999999999999 | 103.31400000000001 | 105.41333333333334 | 93.59333333333332 | 109.08799999999999 | 109.15999999999998 | 129.26600000000002 | 141.21 | 108.21 | 118.7825 | 138.63666666666666 | 117.23 | 143.9975 | 114.96333333333332 | 151.60666666666668 | 120.57 | 151.8725 | 141.89999999999998 | 149.63250000000002 | 128.88200000000001
 | 103.4489 | 103.2677 | 130.7838 | 86.4926 | 114.0912 | 88.5876 | 88.2219 | 108.1505 | 126.4781 | 110.2012 | 144.4741 | 136.5982 | 122.4025 | 136.551 | 142.6967 | 150.112 | 131.9887 | 119.4836 | 154.851 | 129.4567 | 133.4231 | 112.2983
 | 0 | 270
Chart: Measured Power (W)
| 108.2825 | 101.10499999999999 | 137.13999999999999 | 103.31400000000001 | 105.41333333333334 | 93.59333333333332 | 109.08799999999999 | 109.15999999999998 | 129.26600000000002 | 141.21 | 118.7825 | 138.63666666666666 | 117.23 | 143.9975 | 114.96333333333332 | 151.60666666666668 | 151.8725 | 141.89999999999998 | 149.63250000000002 | 128.88200000000001
 | 88.8401 | 91.3001 | 149.4297 | 88.5016 | 116.4431 | 98.6929 | 90.5603 | 109.3175 | 129.561 | 117.3104 | 112.6053 | 120.8134 | 122.5466 | 148.4604 | 84.9703 | 108.8937 | 136.3493 | 154.5452 | 137.447 | 119.6688
 | 0 | 270
Chart: Measured Power (W)
| 145.04285714285714 | 132.75 | 166.71 | 119.81666666666668 | 173.35500000000002 | 117.37666666666667 | 167.4425 | 126.64999999999999 | 157.76999999999998 | 166.86500000000001 | 118.62759999999999 | 163.49333333333334 | 172.56333333333336 | 175.45499999999998 | 173.26666666666668 | 159.4366666666667 | 172.84 | 156.26 | 170.56 | 174.62666666666667 | 175.53 | 137.49166666666667 | 160.9675 | 116.52 | 145.14500000000001 | 133.56
 | 127.218 | 118.5973 | 159.0909 | 148.3761 | 149.055 | 111.7233 | 107.0645 | 129.8581 | 160.4841 | 165.8879 | 181.8061 | 115.5667 | 144.8667 | 164.1342 | 154.805 | 136.8136 | 181.2239 | 156.26 | 165.7295 | 176.6259 | 179.0007 | 162.0985 | 122.9042 | 135.7142 | 158.286 | 158.3497
 | 0 | 270
Chart: Measured Power (W)
| 145.04285714285714 | 132.75 | 166.71 | 119.81666666666668 | 173.35500000000002 | 117.37666666666667 | 167.4425 | 126.64999999999999 | 157.76999999999998 | 166.86500000000001 | 163.49333333333334 | 172.56333333333336 | 175.45499999999998 | 173.26666666666668 | 159.4366666666667 | 172.84 | 170.56 | 174.62666666666667 | 175.53 | 137.49166666666667 | 160.9675
 | 131.533 | 127.6504 | 162.2541 | 164.1454 | 165.9934 | 140.1867 | 124.4745 | 145.9105 | 181.5161 | 185.54 | 137.014 | 146.3389 | 167.8374 | 158.4729 | 131.2003 | 169.4897 | 203.6643 | 200.3537 | 196.7463 | 171.7697 | 135.3268
 | 0 | 270